## Slide 1
PULSEOPS DASHBOARD
React and TypeScript telemetry portfolio
Architecture and implementation overview Application focus: Junior Frontend / React React 18, TanStack Virtual, Web Workers, Zustand

## Slide 2
PROJECT PURPOSE
Telemetry display and responsive interaction
Synthetic telemetry
The worker generates demonstration events every 20 ms.
Example metrics do not represent a deployed service.
No live WebSocket backend is connected.
Growing event history
The store retains up to 60,000 log records.
Rendering the entire history would create many DOM elements.
Virtualization limits rendering to a viewport range.
Implemented approach
Worker generation, validation and 150 ms batching.
Virtualized rows with search and severity filters.
Editable threshold with optimistic update and rollback.

## Slide 3
WORKER PIPELINE
Generation, validation and batching
Worker responsibilities
Generate synthetic events outside the React main thread.
Validate optional incoming objects or JSON strings.
Reject malformed records before adding them to the buffer.
Send buffered records to the UI every 150 ms.
React lifecycle
The hook starts one worker and receives record batches.
The store adds batches in newest-first order.
Cleanup terminates the worker when the component unmounts.
The record cap bounds history size, not total browser memory.

## Slide 4
VIRTUALIZED VIEW
Rendering a bounded viewport
TanStack Virtual
The scroll container has a fixed 600 px height.
Rows use an estimated height of 40 px.
Overscan adds 15 records around the visible range.
Positioned rows occupy a wrapper sized for the full list.
Performance limits
The number of mounted rows depends on viewport and overscan.
Filtering scans the retained records and uses memoization.
No measured FPS, heap or Lighthouse results are claimed.
A larger workload needs profiling on documented hardware.

## Slide 5
STATE OWNERSHIP
Zustand and TanStack Query
Telemetry state
Zustand owns logs, search text and selected severity.
Immutable batches update the retained record list.
Clear resets the current log buffer.
Metrics are labeled as demonstration values.
Configuration state
TanStack Query owns the demo alert configuration cache.
A local asynchronous adapter imitates read and save operations.
The mutation snapshots the cache before updating it.
Configuration persists in memory until page reload.

## Slide 6
OPTIMISTIC UPDATE
Visible save and failure behavior
1. Edit and submit
The form accepts a positive latency threshold.
The save action updates the query cache immediately.
The active threshold reflects the optimistic value.
The save button disables during the request.
2. Demo persistence
The local adapter waits 300 ms before completing.
A checkbox deliberately simulates a save failure.
No HTTP request or notification service is connected.
3. Rollback
The mutation restores the previous cache on failure.
An alert explains the failed save.
A status message confirms a successful save.
Refetch synchronizes the cache with the demo adapter.

## Slide 7
TESTING AND ACCESSIBILITY
Implemented checks and remaining work
Interface accessibility
Search and clear controls have accessible names.
Severity buttons expose their pressed state.
Save results use status messages and errors use an alert.
A full WCAG audit remains future work.
Test coverage
Vitest checks parsing, history retention and empty rendering.
A component test checks save success and failure rollback.
A Playwright scenario covers streaming, filtering and rollback.
Strict TypeScript compilation checks the application source.

## Slide 8
INTERVIEW DISCUSSION
Design choices and extension points
Architecture tradeoffs
Why use a worker? It moves generation and ingestion work away from the UI thread.
Why virtualize rows? It reduces DOM work while retaining searchable history.
What remains on the main thread? Store updates, filtering and React rendering.
Next engineering steps
Connect an authenticated WebSocket source with reconnect handling.
Replace the in-memory configuration adapter with an API.
Profile filtering and rendering under a repeatable workload.
Audit keyboard, screen reader and mobile interaction.